## Slide 1: Hierarchical routing

## Slide 2: Hierarchical routing ??
Because of the global nature of Internet system, it becomes more
difficult to centralize the system management and operation.
For this reason, the system must be hierarchical such that it
is organized into multiple levels with several group loops connected
with one another at each level.
And simply that division is what we call as hierarchical routing.

## Slide 3: How it works:
As mentioned in the previous slide the internet is divided into networks,
each one of these networks is called as autonomous system (AS) and each network contains groups of routers that are connected to one another with routers that are called gateways. Each AS can have different routing protocols, that’s why they are called autonomous. The protocols used in the same AS are called “intra-AS” routing protocols, and “inter-AS” routing protocols are used for communication between different groups of routers.
Sometimes when networks are huge it might be necessary to
divide even further by adding clusters, zones etc... to the
hierarchy.

## Slide 4: Why HR ?
As internet grew up, it became inefficient and even impossible to store all destinations in routing tables so instead, hierarchical routing took place which made it so that tables can be held as small as possible, and things can get easier to manage and maintain.
Also, it is what used in practice because in “link state” and “distance vector” algorithms we were talking ideally where all routers are identical, and network is “flat”.

## Slide 5: Interconnected ASes
forwarding table configured by both intra and inter-AS routing algorithms.
intra-AS sets entries for internal destinations.
inter-AS & intra-AS sets entries for external destinations.
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
Forwarding table:
Gateways

## Slide 6: Inter-AS tasks:
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
AS1 must:
learn which destinations are reachable through AS2, which are reachable through AS3.
propagate this reachability info to all routers in AS1(itself)
job of inter-AS routing!

## Slide 7
Example: setting forwarding table
in router 1d
Suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c), but not via AS2
  inter-AS protocol propagates reachability info to all internal routers.
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c
  installs forwarding table entry (x, I)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…

## Slide 8
Example: choosing among multiple ASes
Now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
To configure forwarding table, router 1d must determine which gateway it should forward packets towards for destination x
this is also job of inter-AS routing protocol!
…
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
?

## Slide 9
Example: choosing among multiple ASes
Now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
To configure forwarding table, router 1d must determine which gateway it should forward packets towards for destination x
this is also job of inter-AS routing protocol!
hot potato routing: send packet towards closest of two routers
learn from inter-AS
protocol that subnet
x is reachable via
multiple gateways
use routing info
from intra-AS
protocol to determine
costs of least-cost
paths to each
of the gateways
hot potato routing:
choose the gateway
that has the
smallest least cost
determine from
forwarding table the
interface I that leads
to least-cost gateway.
Enter (x, I) in
forwarding table

## Slide 10: Advantages of HR:
The routing table size in each router will be greatly reduced.
Routing stability will be improved.
Reusable locator address space.
Support communication between heterogeneous networks.
Simple to organize and maintain.

## Slide 11: Thank You!
Muhammed Nur Aldın HALUBİ
2018556301

## Slide 12: References:
Textbook: Computer_Networking_A_Top-Down_Approach_6th_edition.
Hierarchical Routing - Computer Notes (ecomputernotes.com).
Hierarchical Routing Architecture.
What is hierarchical routing? (tutorialspoint.com).